Dear All,

please find in attachment a short description of modifications in the DCS

software in the SR1 building, which were done in the period 03.03.05 - 23.03.05.

There were the following activities:

- temperature Motherboard and ELMB was moved to EndCap Wheel A.

- main panel view was changed accordingly to needs;

- temperature button for temperature monitoring of EndCap Wheel A was added;

- a low voltage panel, which allows controling voltages in 2 independent sets from one bulk PL500, was added;

- new panels for monitoring low voltage software interlock were added;

- minor changes were done in the high voltage part:

o when any high voltage channel is switched on - the information is displayed on the main panel. There is also a possibility to switch off high voltages in the whole crate in case of emergency by pressing button with that information.

o also information on the high voltage test panel is displayed, with a possibility of emergency switching off of the high voltage in one board.

o display of instantaneous values of monitor current was added in the high voltage test panel.

o retrieving of high voltage test in case of any interruption (program or PC crash).

The up-to-date description will be placed in EDMS soon.

Please contact me in case of any problems, suggestions, questions.

Elzbieta