Minutes & action items from August 16 TRT Barrel integration meeting.

1) Check on old action items:

- P1.25 cooling sleeve replaced.

- Ultem screw: Jack to talk with vender for recommendation between cheese head and socket head option.

- Active gas system to be assembled for flow rate test and HV test.

2) Type 2 modules installation & tests

- 9 modules installed and half way through testing

- 13 more modules available for insertion.

3) Module delivery from 154

- 18 modules under test, changed current limit to 20uA and use 1Mohm resistor in HV line.

- Expecting 2-3 modules in 2 weeks.

- Hopefully release all type 2 modules middle of Sep.

4) Purging gas gasket

- 1/8", 1/16" available. Looking for 3/32", 1/32".

5) Fuse box brackets & barrel envelope

- John will look at drawings from Curt and check for violation of envelope for extending fuse box bracket 8mm in z.

- Still waiting for Type 3 cooling plates to check consistency.

6) Electronics tests on P1.29.

- Getting the database ready. In the mean time trying to run tests on the module.

- Reconsidering source test. Perhaps more useful thing is to get trigger-capable patch panel and look at cosmic ray (?)

- In addition: 17 modules worth of electronics in hand. 20 triangles assembled.