Minutes on Dec. 07, 2005 TRT Barrel integration.

- Fuse boxes:

  - All, but 2, side A fuse boxes are installed. 3 stacks tested so far. The testing process turns out taking longer than expected due to adjustments and checking on passport for no contact channels. Expect to finish side A this week.

  - All bad (37) fuses replaced. Still need to be coated, and baked if current draws are high.

  - Ben is going to look at the data to find out when the bad fuse on stack 8 occurred.

  - The 2 spare fuse box sets being made at Duke are expected to finish this week.

  - There were worries that when a fuse is blown and shorted to ground due to broken wire can cause instability in the fuse box. Chiho will do a test on the old fuse boxes.

- Manifold:

  - IU is waiting for Curt’s drawing to send to their machine shop. As of this morning it’s not there yet.

  - Duke machine shop is working on the parts. Will try to finish before Christmas and let Jack bring to CERN ~Jan. 4. The 2 cooling hubs will be made first.

  - For system test we would like to install 4 spines (2 front, 2 back) at the lower sectors. The best would be to install 8 spines for both upper and lower sectors, but we have to see what parts are available after New Year. We have until Jan 15 to install them.

  - There were some discussions on cooling leak spec and test procedures. The allowance on coolant loss is 500kg/year = ~ 15%/year

  - Harold circulated peek forming procedures. Some questions were raised e.g. how long is the tube kept in heating? How do we prevent water from getting in the tube …etc. Harold wasn’t in the meeting, so this will be answered offline.

- Thermal sensors:

  - All installed and wires fixed, however, the Toshiba compound used didn’t cure and at risk of getting transferred everywhere. Suggestion was made to coat them over with conformal coating to harden them. But, this needs to be tested before applying. Zbyszek was absent from the meeting and made a written comment. Please see below.

- At some moment we have realised that fixing the sensor cables to prevent them from being broken at the level where they 'enter' heat shrink tube with the Araldit Rapid is not a best way. The reason was that if one has to exchange the FE board there is a substantial risk that cable gets broken since Araldit forms a very solid joint. So we have attached cables to the cooling plates only with Araldite and decided to fix it to space frame with something which can be easily broken. The natural choice was a silicon compund which when cured is rather elastic and is forming not a  very solid joint.

There was no time for a 'research' so we have chosen a silicon sealing compound available at CERN stores. The specifications are in  attached files.   I must admit that I did not studied this documents very carefuly (bad resolution) but stoped after statements:  'rapid polymerisation', 'non corrosive', 'non irritant', and (here I have to quote French ) 'hors poussiere' after 5 min.  With this specs in mind I have talked to Anatoli (silicon !!) and he agreed.

After application (on Friday) it turned out (on Tuesday) that many joints are not cured (yet), are 'hors pousierre' but not solid enough to stand   manipulation. Then I have studied deeper the specs. There is no spec on 'minimal' humidity  or 'minimal' temperature. But the curves show that at low relative humidity (~30 %) curing can take few days depending on the thickness.  Our 'blobs' are max 5 mm thickness which means that curing goes slowly (> few days). Humididty in the SR1 is ~ 33 %.  This are facts ! Now subjective view (mine).

I do not agree with the statement  that the compound is 'everywhere' !  I talked to Jack who has been mounting fuse boxes and he says that he even did not noticed that  something there is sticky. We have moistured today (morning) the joints on one face and I think this should drasticaly speed up the curing. Final answer we will get tomorrow (latest Friday). I have no opinion on formal coating but since curing speed depends on humidity to cut off the compound from environment might even stop curing.

I will keep you (community) informed.

If this problem is solved  the sensors are installed, calibrated and labeled. Prepared for final integrations with harnesses.

Best regards Zbyszek

(Spec. sheets attached, next 3 pages)